## Slide 1: Volumetric Capture
Marcel Bruckner, Kevin Bein, Moiz Sajid

## Slide 2: Goal
Frame Fusion

## Slide 3: Setup
4x Intel RealSense Depth Camera D415
4x Tripods
USB Hub
USB Active Repeater Cables

## Slide 4: Setup Problems
4x cameras are not working with single USB-Hub
Multiple Repeater Cables not working
Therefore, 3x cameras only

## Slide 5: Pipeline Overview
RGB and depth frame capture
Post-Processing
Align RGB and depth frame
ChArUco Board detection
Callibration via Procrustes, Bundle Adjustment and ICP
Fusion into Voxelgrid
Compute Marching Cubes

## Slide 6: 1. RGB and depth frame capture
1280x720 active stereo depth
1920x1080 RGB resolution

## Slide 7: 1. RGB and depth frame capture
1280x720 active stereo depth
1920x1080 RGB resolution

## Slide 8: 2. Post-Processing
2.2 Threshold Filter
2.1 Raw Input
librealsense
Camera

## Slide 9: 2. Post-Processing
2.2 Threshold Filter
2.3 Hole-Filling Filter
2.1 Raw Input
librealsense
librealsense
Camera

## Slide 10: 3. Align RGB and depth frame
librealsense

## Slide 11: 4. ArUco markers
Encodes messages (in our case: 1, 2, 3, 4, ...)
Can be easily detected
Position of edges are known

## Slide 12: 4. ChArUco
Combination of multiple ArUco markeres on a chessboard = ChArUco

## Slide 13: 4. ChArUco board detection
Detect 12 ChArUco corners in all camera streams

## Slide 14: 4. ChArUco board detection
Detect 16 ArUco markers on one board
Single board
All camera streams

## Slide 15: 4. ChArUco board detection
Detect 16 ArUco markers on one board
Low resolutions only
Noisy depth maps did not work too well during calibration

## Slide 16: 4. ArUco cube detection
Ultimately, big cube with single ArUco marker on each side
[big cube picture here]

## Slide 17: 5. Calibration via Procrustes and Bundle Adjustment
OpenCV:
  cv::aruco::detectMarkers
  cv::aruco::estimatePoseCharucoBoard
Returns: Rotation and translation matrix
Use detected ArUco corners as correspondences to refine rotation and translation matrices

## Slide 18: 5. Calibration via Procrustes and Bundle Adjustment
Use detected ArUco corners as correspondences to refine rotation and translation matrices
Initialize algorithm with Procrustes
Minimize re-projection error (Bundle adjustment)

## Slide 19: 5. Calibration via Procrustes and Bundle Adjustment
Initialize algorithm with Procrustes
ArUco correspondences
Minimize rotation and translation

## Slide 20: 5. Calibration via Procrustes and Bundle Adjustment
Minimize re-projection error (bundle adjustment)

## Slide 21: 5. Calibration via Procrustes, Bundle Adjustment and ICP
Run ICP for further refinement

## Slide 22: 6. Fusion into Voxelgrid
Calculate TSDF values
Fuse aligned points into Voxelgrid

## Slide 23: 7. Compute Marching Cubes

## Slide 24: 7. Compute Marching Cubes

## Slide 25: Future work
ICP to further improve Calibration
Edge Enhancements and artifact reduction

## Slide 26: Implementation Details
Librealsense API
  Camera communication
  Post-processing filters: Hole-filling, Depth threshold
  RGB and Depth alignment
OpenCV for ChArUco corner detection
OpenGL Rendering
OpenGL Shading Language
Immediate Mode GUI (imgui) for UX

## Slide 27: Implementation Details
Custom implementation of Procrustes, Bundle Adjustment and ICP using Ceres solver and Eigen
Custom implementation of Marching Cubes
Not used:
  Point Cloud Library (PCL)
  CUDA
  DirectX

## Slide 28: Implementation Details
Custom implementation of Procrustes, Bundle Adjustment and ICP using Ceres solver and Eigen
Custom implementation of Marching Cubes
Not used:
  Point Cloud Library (PCL)
  CUDA
  DirectX

## Slide 29: Live Demo
Please feel free to join us in our office for a Live Demonstration!

## Slide 30: Volumetric Capture
Thank you! Questions?

## Slide 31: Pipeline Overview
RGB and depth frame capture
Post-Processing
Align RGB and depth frame
ChArUco Board detection
Callibration via Procrustes, Bundle Adjustment and ICP
Fusion into Voxelgrid
Compute Marching Cubes