## Slide 1: 3D Scanning and Spatial Learning Volumetric Capture
Marcel Bruckner, Kevin Bein, Moiz Sajid

## Slide 2: Volumetric Capture
Realtime 3D reconstruction using multiple cameras

## Slide 3: Reconstruction Pipeline
RGB-D frame capture
Voxelgrid TSDF
Marching Cubes surface
Correspondence matching
Camera calibration

## Slide 4: RGB-D Frame Capture
Hardware setup
4 Intel RealSense Depth Camera D415

## Slide 5: RGB-D Frame Capture
1920x1080 RGB resolution
1280x720 active stereo depth
Frame aquisition

## Slide 6: RGB-D Frame Capture
Original
Threshold filtered
Depthmap preprocessing

## Slide 7: RGB-D Frame Capture
Final pointclouds
Add video of single pointcloud

## Slide 8: RGB-D Frame Capture
Tried approaches
Holefilling filter
Spatial filter
Edge enhancement filter
Add images of different filters

## Slide 9: RGB-D Frame Capture
Difficulties
Bandwidth limitations

## Slide 10: Correspondence Matching
ArUco markers
Square markers with unique ids
Easy detection using OpenCV
Subpixel perfect corners in color stream

## Slide 11: Correspondence Matching
Marker cube
6 sides, one marker per side
Easily detectable even from steep angles
Overlap of detected markers used for pose estimation

## Slide 12: Correspondence Matching
Marker cube

## Slide 13: Correspondence Matching
Tried approaches
ChArUco marker board
Allows simultaneous marker detection and pose estimation
Tradeoff between number of markers and marker size
Not robust enough

## Slide 14: Camera calibration
3D marker positions
Backprojection of ArUco markers into 3D pointcloud
Subpixel perfect pixel location allows robust backprojection
Align 3D marker positions of all cameras

## Slide 15: 3D Pose Estimation
Procrustes
Align two objects using known correspondences
Translation: Vector between centers of gravity

## Slide 16: 3D Pose Estimation
Procrustes
Align two objects using known correspondences
Scale: Avgerage distance to center of gravity

## Slide 17: 3D Pose Estimation
Procrustes
Align two objects using known correspondences
Rotation:
  minimize
  Compute SVD of Cross-Covariance matrix:
  Final rotation:

## Slide 18: 3D Pose Estimation
Procrustes
Procrustes is not robust enough
MSE after alignment still fairly high

## Slide 19: 3D Pose Estimation
Point to Point Error
Use procrustes as an initialization
Optimize:

## Slide 20: Camera Calibration
Difficulties
Visualization of calibration results
Ceres for Point to Point optimization
Further work
FLANN for correspondence matching
ICP for further alignment

## Slide 21: Voxelgrid
Aligned frames get fused into voxelgrid
Calculate TSDF of the integrated frames
Weighted averaging of the TSDF values
Implicit surface representation

## Slide 22: Voxelgrid
Aligned frames get fused into voxelgrid
Calculate TSDF of the integrated frames
Weighted averaging of the TSDF values
Implicit surface representation

## Slide 23: Voxelgrid
Difficulties
CPU approach as a proof of concept
Move all calculations to GPU for parallelization
Had to learn OpenGL compute shader programming for realtime
Tradeoff between resolution and frame rate
Find good truncation distance to lower artifacts

## Slide 24: Marching Cubes
Converts an iso-surface of a tri-variat scalar function to a polygonal mesh
Uniform sampling (Voxelgrid) of the implicit surface
Determine zero crossings for every grid cell

## Slide 25: Marching Cubes
Final result is a triangulated mesh representing the implicit surface

## Slide 26: Marching Cubes
Difficulties
CPU approach as a proof of concept
Move all calculations to GPU for parallelization
Had to learn OpenGL compute shader programming for realtime
How to approach uninitialized voxels
2-pass compute shader to tackle memory issues

## Slide 27: Final results

## Slide 28: Volumetric Capture
RGB-D frame capture
Voxelgrid TSDF
Marching Cubes surface
Correspondence matching
Camera calibration
If you are interested in a live reconstruction of yourself, feel free to come to our office at 02.07.31!